## Slide 1
M28 Omni-Purpose Module

## Slide 2
M28
The final STM building block

## Slide 3
The four STM modules
M28
Omni-Purpose Module
B112
Bass Module
S118
Sub Module
M46
Main Module

## Slide 4
4 x 6.5 inch LF/MF Flat Membrane Drivers
4 x HF Ketone Polymer Compression Drivers
Frequency response: 85Hz–20kHz
145dB peak SPL
H350mm/W575mm/D715mm
Dispersion 90˚ H x 0-10˚V
M46 Main Module

## Slide 5
1 x 3000W +/- 3cm excursion 12 inch LF Driver
143dB peak SPL
Frequency response: 55Hz-200Hz
H350mm/W575mm/D715mm
B112 Bass Module

## Slide 6
1 x 3000W 18 inch LF Driver
143dB peak SPL
Frequency response: 25Hz-120Hz
H700mm/W575mm/D715mm
Flown or groundstacked
Omni or CD/RS cardioid modes
S118 Sub Module

## Slide 7
2 x 8 inch long excursion LF Drivers
2 x HF Ketone Polymer Compression Drivers
141dB peak SPL @ 1m
Frequency response: 60Hz-19kHz
H234mm/W575mm/D653mm
M28 Omni-Purpose Module

## Slide 8
M28 in detail

## Slide 9
Same polyurethane composite weatherproof construction as M46 and B112

## Slide 10
Horizontal dispersion user-configurable
90 or 120 degrees
90º
120º

## Slide 11
Peak output of 141dB @ 1m in 90 degree dispersion mode
2dB louder than GEO T!
Possibly the most powerful cabinet in its class

## Slide 12
Same width as all STM modules

## Slide 13
Two-thirds the height of M46 and B112

## Slide 14
Compatible with all STM dollies and rigging

## Slide 15
Omni-purpose capability

## Slide 16
M46 Downfill

## Slide 17
When used as M46 downfill, M28 is attached below the STM bottom bumper in tension (gravity) mode

## Slide 18
Available angles in downfill mode are 10, 12.5, 15 degrees

## Slide 19
M28 as a Main PA

## Slide 20
M28 as a Main PA
Fully compatible with all STM modules and rigging

## Slide 21
1 x S118 : 1 x B112 : 2 x M28
Recommended starting ratio

## Slide 22
M28 is flown using compression mode

## Slide 23
60Hz – 20KHz
Usable alone for speech and light music events

## Slide 24
Full-range flown system
(30Hz to 20 kHz)
3 x S118 and 6 x M28

## Slide 25
Or with subs on the floor
6 x M28
6 x S118 groundstacked

## Slide 26
Full-range system with extra “punch”
3 x B112, 6 x M28
3 x S118 groundstacked

## Slide 27
Groundstacked
Powerful, full-range system with extremely small footprint
1 x S118, 1 x B112
3 x M28

## Slide 28
Venues with rigging weight limitations

## Slide 29
1 tonne point restriction
18 x M28 single column. Total cabinet weight = 666kg

## Slide 30
6 x B112 + 12 x M28
Total cabinet weight = 798kg
1 tonne point restriction

## Slide 31
9 x M28
Total cabinet weight = 333kg
500kg point restriction

## Slide 32
3 x B112 + 6 x M28
Total cabinet weight = 399kg
500kg point restriction

## Slide 33
Amplification

## Slide 34
M28 active
2 NUAR channels powers up to 3 cabinets

## Slide 35
8 ohm cabinet
Up to 12 M28 cabinets on one NUAR rack (STM standard)

## Slide 36
Packaging

## Slide 37
Lightweight dolly for smaller applications

## Slide 38
Compatible with STM dollies, roofs and covers

## Slide 39
12 x M28 on a STM double dolly

## Slide 40
Designed and built from the ground up as an STM module, M28 is a “future-proof” solution for smaller companies with plans to grow

## Slide 41
Thank you